## Slide 1
10.149.31.12
10.149.18.252
mPing - tool to show the reconfiguration time

## Slide 2
Right mouse click - edit
In our example: Change it to mpingLCD.exe –z50–w50 –tsu 10.149.31.12
mPing - edit the parameters

## Slide 3
Options:
-n count number of echo request to be sent during one loop (4)
-l length length of buffer (in bytes) to be sent 4..65500 (32)
-w timeout timeout in milliseconds waiting for the reply (1000)
-z time time in milliseconds between packets (1000)
-m retries how often a ping is repeated before timeout (0)
-i lost lost echo requests before counting interruptions (0)
-x inc increment destination IP address by 'inc' (0)
-o count number of pings before the IP addr. is incremented (1)
-T time sending pings continuously - loop time in sec. (none)
-N loops max. number of ping loops (unlimited)
-Z time time in seconds between loops (0)
-t sending pings continuously to the host - loop (off)
-s show only ping statistics (off)
-g show current time instead of time since start (off)
-u new line in output for each interruption (off)
-a count ICMP errors and corrupted as interruptions (off)
-e statistics overview when terminating program (off)
-E interruption overview when terminating program (off)
-k block keyboard (off)
-q quiet mode, header & trailer only (off)
-Q strict quiet mode, no screen output (off)
-d the contents of all packets is displayed (off)
-U output only unreachable IPs (in stat. mode, too) (off)
-y beep once when an interruption has been detected (off)
-Y beep on interruption (for every lost packet) (off)
-r UDP receiver mode for IP address (source) (off)
-c UDP transmitter mode for IP address (dest.) (off)
-p port UDP port number for receiver and transmitter +1 (18200)
-f file name name of log file for ping statistics (none)
-b file name name of file with ip address list (none)
-B append hostname to ping result line (off)
-v display messages for ip address list file (off)
-V same as -v, display also debug messages (off)
-W write resolved IP list host addr. to cache file (off)
-H displays more help on IP list file processing (off)
Special keys during statistics:
<ESC> quit
<CR> reset statistics
<Space> display statistics overview
Syntax: MPing [-?htsguaeEkqQdyYrcUvVBH] [-n count]
[-l length] [-w timeout] [-z time] [-m retries]
[-i lost] [-x inc] [-o count] [-T time] [-N Loops]
[-Z time] [-p port] [-f file]
[-b file] [-W file] IP address
mPing - parameters definition

## Slide 5
10.149.31.12
10.149.18.252
After these settings ---- You can start
1. Double click (start)
3. This clock start
and stop when
the reconfiguration is finished
2. Interrupt this link